## Slide 1: Serving the 3G Network
FORCES Project Colloquium
Martin Cookson
BTexaCT
martin.d.cookson@bt.com
forces_a.ppt
Notes: Like many of you I have been involved in IN for a number of years - and probably like many of you I have been considering the impact of the internet and considering the question of do we need intelligence in the future IP networks and if yes what does it look like and does the IN we own today play any part in it. Hopefully this presentation will provide some answers to this question and provide one of the possible futures in the uncertain world that Olivier defined for us yesterday.
Although my presentation is called the future of intelligence I will occasionally use the term service control since there tends to be a negative connotation attached to IN and intelligence.

## Slide 2: Overview
Commercial Environment
Network Evolution
Future Intelligent Strategy
Intelligence Technologies
  SIP services
  3G Service Control
  Integration
Open Networks
Service Creation

## Slide 3: Changing Market Environment
PSTN Network [costs]
PSTN Business [revenue]
0
200000
400000
600000
800000
1000000
1200000
1400000
1600000
1997
1998
1999
2000
2001
2002
2003
2004
2005
Data
Voice - Mobile
Voice - Fixed
Terabytes/yr
Source: OC&C
Wholesale
growth
CPS
Calls
Only
LLU
Regulation
increased
volumes
lower
margins
massive
shift to data
Dial IP
shift to mobile voice,
competition
competition
Disruptive Technologies
New markets, solutions,
operating models
Technology
Lower
cost
alternatives
Notes: Well understood
key messages :
greater wholesale traffic leading to lower margins
erosion of current business due to increasing competition particularly mobile voice
regulation provides increased competition and in particular LLU allows several telephony channels to be provided
changing mix of traffic to be data dominated provides both a challenge for the network and an opportunity

## Slide 4: 3G Costs
£ 68 Billion spent on 3G licenses to date in Europe
Average of £2 billion per operator to build network
Drastic increase required in mobile revenues
Cannot be achieved just by voice
Essential to offer new services
Information World Review, 01-Nov-2000, Reuters
Notes: Approx 110 billion Euros
One of the most important factors in network evolution is the interest and investment in 3G networks. As of last Thursday operators had spent £68b (about 110 B E) in Europe a lone. Combined with this it will cost about £2B per network per operator to build these 3G networks.
In order to get a return on this investment there needs to be a drastic increase in mobile revenues - but as somebody pointed out yesterday revenues per subscriber for voice are actually decreasing.
Hence there will have to be a lot new services being provided that will allow more encourage more spend by the subscriber.
Now while the majority of these will be content based services there will be a demand for conversational, real time services. Hence 3G represents anew stimulation for more services.

## Slide 5: Packet Based Voice Networks
Existing
transmission
systems
are reusable
Common
data &
voice
network
Inevitability
&
consensus
Supplier
push -
enterprise
market
saturated
IP Telco Network
Internet
Core IP N/W
Intranet
Extranet
Support
carrier
grade
telephony
Justifiable on
new services
since does
not lower
costs
Continue
existing
telephony
services
Customer Demands
Integrated services
Mobility
Personalisation
Ease of use
Multiple Access
ADSL
WDM
ATM/SDH
GPRS & UMTS
Analogue/ISDN

## Slide 6: Network Evolution
PSTN
GSM
Enterprise
independence
Internet
ATM
Managed IP
Hyperlan
H.323
SIP
3G
Internet
telephony
Packet based networks
Circuit switched
networks
IP VPN
Transport
Call control
Notes: Service control is about how we provide services controlling the network resources - so we must consider what these networks are.
There is a very important difference between the circuit switched networks of today compared to packet based networks. This is the separation of call control and the bearer control or transport. This means that service platforms can interact with the call control but don’t need to handle or trombone the bearer traffic.
So while a whole myriad of networks are developing e.g. internet telephony, 3G network or voice over ATM from a service control it is actually alot simpler. In the IP world there are is either H.323 and SIP and SIP seems to be dominating as the most enduring technology.
I will show later on how services can be realised with SIP.

## Slide 7: Staged Service Control Strategy
1 : IN Evolution
Selected evolution of current intelligence
service continuity for voice services
review service profitability
2 : Soft Intelligence
Introduce soft intelligence solutions
exploit IP technologies
range of intelligence configurations
3 : Intelligent Data
Improvements
Intelligence is not just about voice
flexible control of IP network
sessions services
Reduce cost base and speed-up delivery
network applications attractive to s/w industry
integrate with CPE
Notes: This slide captures the scope of the strategy as a whole. For convenience I have split it into 3 areas:
IN Evolution : as we create new IP networks we will need to carry forward some of the existing IN. This is either for reasons of service continuity or revenue continuity. This is enabled by many of the existing IN systems having ready interfaces to connect into future call servers. For example we will expect to still want to have CAMEL capability in 3G networks to provide pre-paid capability. This evolution MUST be subject to review and the extent will be limited.
Soft Intelligence : Recognise that the IP network is different and harness IP technologies as well as IN principles. Service control is provided from servers on the IP network and there is a range of configurations; from large number management systems to PC based call

## Slide 8: What is it?
SIP is the
Session Initiation Protocol
IETF RFC 2543
“ … an application-layer control (signalling) protocol for creating, modifying and terminating sessions with one or more participants.”
Notes: SIP is from the IETF and is increasingly becoming the technology of choice for building future networks.
It is characterised by being simple, uses text, extendable modular and adopts a more web approach to the creation of services.

## Slide 9: SIP services
Classic supplementary services
Classic IN services
Third-party call control
Finding a person / person-dependent routing
Multi-party services / conferencing
Multicast services
Integration with other internet applications
Services can be implemented by anybody
- in the network or at the edges
Notes: SIP provides many ways to build services. Everything from simple supplementary services such as divert on busy through to integration with internet applications. It is also possible to support IN services such as number translation
Inherently it supports multi-party communication and has location services I.e. you have to register before you can start to communicate in order to inform the network at which address you are at.
So while SIP provides a platform for operators to implement service in a way that they are used to it is also a technology that is accessible to a much larger population hence you need to be quick to implement.

## Slide 10: SIP Service Control
IP Network
SIP
client
Home
Subscriber
Server
Application
Server 1
Application
Server 2
Application
Server 3
SIP proxy action
Call
Server
CPL
CGI
SIP
servlet
executables
JAVA
Java applet
attachment
SIP invite
CPL= Call Processing Language
CGI = Common Gateway Interface
JAIN = JAVA Integrated Networks
J A I N

## Slide 11: 3GPP Release 2000 Network
PSTN / ISDN
MGW
PSTN
IP
ROUTER
SGW
IP Core
HOME SUBSCRIBER SERVER
CALL SERVER
CALL SERVER
APPLICATIONS
GPRS
E-SGSN
GPRS VLR
E-GGSN
DHCP DNS
Radius
UTRAN
RNC
RNC
Location
management
JAVA RMI
CAP over IP
SIP (network)
SIP (network)
ISUP
SIP / SIP-T ISUP over IP
SIP (access)
Notes: This is the 3GPP release 2000 network. It consists of the radio network. This connects into an IP core using enhanced GPRS - this in effects deals with the mobility and allocates an IP address into the IP core. It could be the case that the IP core is accessed via a fixed access interface
The call servers - called Call State Control functions provide the call or session control. The HSS is an evolved HLR which in addition to providing mobility management also provides profile download services. There is gateways to deal with the media and signalling conversion to access other TDM or IP networks.
Our interest is how the applications link into the call severs and how the HSS is used to personalise services.
SIP is used at the access and in the network core. A variant of SIP called SIP-T (which encapsulates ISUP ) is used to talk to the PSTN. The area of debate at the moment is the definition of the interfaces between the call server and the application space - this is covered in more details in the next slides.

## Slide 12: 3G Service Control Requirements
Flexible range of control interfaces
Evolution of CAMEL
Mobility and roaming
Customer profile based services
Service provision by home or visited network
Notes: These are some of the requirements that are driving the development of service control in the 3G network
Striving for flexibility to cover: evolution, exploitation of SIP and appealing to a wide community of developments.
CAMEL specifically as it deals with Roaming and it is the default solution for certain services e.g. pre-paid.
Mobility and roaming - need to be able to access services when roamed into another network.
Looking for a more user focused slant to the services - I want to download my profile to wherever I roam and have my environment.
There is a great debate over home or visited network service control. I want them both - clearly I want to serve my customers with my servers but I also want to serve all he customers that roam into my network. If I am in Barcelona to select tapsRus - BTcellnet are unlikely to make sense of this while I am sure Airtel can adequately provide the services.

## Slide 13: Call Server Interfaces
Home Subscriber
Server
Serving
Profile
Database
Application
Server
Application
Server
CAMEL
Service
Environment
API
Mapping
Function
IpSSF
State
Machine
Message
Processor
SIP
Session Control
SIP Server
Call
Server
Location
management
& profile
download
Cx
SIP
API
CAP
CAP = CAMEL Application Protocol
IpSSF = IP Service Switching Function
3rd Party
Application
Server
OSA

## Slide 14: Integrated applications
IP
Call
Server
Audio
Server
Location
Server
Telephony & real-time domain
Conferencing
Server
Non-integrated,
replication,
missed opportunity,
WWW
Server
Directories
Email
server
authentication
software
Application
software
games
server
Internet & multi-media domain

## Slide 15: Integrated applications
IN
IP
WWW
Server
Directories
Email
server
authentication
software
Application
software
games
server
Call
Server
Audio
Server
Location
Server
Conferencing
Server
APIs
APIs
APIs
Terminal
capabilities
New
Application
JAVA based
service creation
MeXe
application
Router
Application
Server
Integrated application domain
Intelligence
domain

## Slide 16: Serving the Network
PSTN
SLEE
App
App
App
Network domain
IN
PSTN
Network domain
gateway
Open API
N/W
App
shared
App
IP Network
3rd Pty
App
3rd Pty
App
3rd Pty
App
3rd Pty
App
3rd Pty
App
Server Provider Domain
Call
server
Open API
N/W
App
Parlay,
JAIN,
OSA

## Slide 17: Parlay in the Network
Network
Security
Boundary
The Parlay APIs
Network
Elements
Enterprise
Domain
Service
Provider
Domain
SCP
Internet
Managed IP
network
Network
Elements
Mobile
Network
Hosted Application
Server
Application
Server
Router
HLR
Parlay Applications
Intranet
Fire
wall
Parlay
Gateway
Parlay
Gateway
PSTN
Network
Elements

## Slide 18: Expansion of Parlay Services
Gateway
API
API
API
API
API
API
API
Framework
Call
Control
Messaging
User
Interaction
Mobility
Content
Based Charging
Connectivity
management
Policy
Management
PARLAY APPLICATION
Parlay 3 Specification
Issued June 2001

## Slide 19: Service Creation Evolution
switch
Embedded software
bundled into switch
by switch supplier
network
IN
IN tools
switch
network
Switch independent,
service creation tools BUT
proprietary and IN specific
Call
server
network
Application
server
API
API
API
Network APIs open
to software industry
using general purpose
tools (C++, JAVA)
S/W tools
SOAP

## Slide 20: Summary
Real time service control has a major part to play in realising an integrated and stimulating experience for the customer & as a secure, profitable, and flexible tool for the provider.
Think broadly and use common technologies
Networks rich in services will come thru open network interfaces.

## Slide 21: Service Creation
Enterprise Java Beans
Simple Object Access Protocol (SOAP)
API sets
Call Processing Language (XML)
Enterprise Application Integration
Mainstream application development
Create for the application server and terminal
SIP Servlets
CPL
SIP
SOAP
Notes: How do you built your components and stick them together.