## Slide 1: Detection and Resolution of Feature Interactions in Telecommunication Systems During Runtime
Dave Marples
Communications Division
Department of Electrical & Electronic Engineering

## Slide 2: Structure of Presentation
Rationale behind the work
(Very) Brief review of existing techniques
Application to new approach
The new technique
Results
Conclusions
  Capabilities
  Limitations
  Future Work
Rationale : Review : Application : Technique : Results : Conclusions

## Slide 3: Rationale
New Techniques being used in today’s networks mean that there is more feature functionality then ever before
This feature functionality is increasingly developed by independent agencies that do not coordinate
This leads to interactions which have to be resolved when features first meet, in the context of existing (legacy) systems
The Objective : To develop Feature Interaction techniques that can be used in runtime, in the context of existing systems
Rationale : Review : Application : Technique : Results : Conclusions

## Slide 4: Review of Existing Techniques
Design Time Approaches
  State Based Models
  Formal Languages and Specifications
  Extended Feature Specifications
  Temporal Logic
Development Approaches
  Behavioral Signatures
  Process Support
  Architectures
Rationale : Review : Application : Technique : Results : Conclusions

## Slide 5: Review of Existing Techniques Continued…
Runtime Techniques
  Feature Managers
  Direct Communication
Problem Reformulation
  Negotiation
Rationale : Review : Application : Technique : Results : Conclusions

## Slide 6: Application
Apply ideas from transactions to allow features to ‘suggest’ responses to an event without them needing to be committed to the hardware.
With the following constraints;
  Minimal knowledge of feature internals
  Can be used in runtime
  Extensible to more than two features
Rationale : Review : Application : Technique : Results : Conclusions

## Slide 7: Technique Overview
Add rollback capabilities to existing features
Create a ‘tree’ of possible posterior states from an initial triggering event
Examine the tree for the best resolution
Record the selected resolution for application next time the scenario occurs
Rationale : Review : Application : Technique : Results : Conclusions

## Slide 8: Technique Add rollback capabilities to existing features…
Rationale : Review : Application : Technique : Results : Conclusions
Feature
To/From
Switching System
Cocoon
Feature
To/From
Switching System

## Slide 9: Technique …in the context of a Feature Manager
Feature
Manager
Cocoon
Feature
Cocoon
Feature
Cocoon
Feature
Cocoon
Feature
Switching
System
Switching
System
Feature
Rationale : Review : Application : Technique : Results : Conclusions

## Slide 10: Technique Using the Cocoon to achieve rollback : COMMIT CASE
Start Transaction
FORK
Event
Response
Response
Commit Transaction
KILL
Process Copy Created
Events/Responses
Result in copy being
modified
Copy now becomes the
‘master’ instance
Rationale : Review : Application : Technique : Results : Conclusions

## Slide 11: Technique Using the Cocoon to achieve rollback : ABORT CASE
Start Transaction
FORK
Event
Response
Response
Abort Transaction
ABORT
Process Copy Created
Events/Responses
Result in copy being
modified
Copy dies and original
resumes – back to initial
state without seeing intervening
messages
Note: Obvious performance benefit here to be gained by only using the copy when rollback needs to be performed, since rollback is (hopefully) the less common case.
Rationale : Review : Application : Technique : Results : Conclusions

## Slide 12: Technique Create tree of possible posterior states
Resolution 3
Rationale : Review : Application : Technique : Results : Conclusions
3
4
6
7
8
2
Responses from more than one feature returned
Initial Event
Response
Resolution 1
5
Resolution 2
1
Responses from one feature returned

## Slide 13: Results Experimental Set
Nine Features based around FIW’98 set;
  Call Forwarding on Busy Line (CFBL)
  Teen Line (TL)
  Terminating Call Screening (TCS)
  Call Forwarding Unconditional (CFU)
  Call Waiting (CW)
  Return Call (RC)
  Originating Call Screening (OCS)
  Hot Line (HL)
  Return Call Immediate (RCI)
Rationale : Review : Application : Technique : Results : Conclusions

## Slide 14: Results Headline Numbers
38 distinct 2-way (Feature to Feature) interactions identified in the sample set.
Of these, 31 were detected automatically, 7 were missed.
Of the 31 that were detected, all could be resolved in some way by the system.
Three ‘real’ three feature interactions were detected in the experimental feature set.
Rationale : Review : Application : Technique : Results : Conclusions

## Slide 15: Results Analysis…
Interaction cases split into four groups;
  Shared Trigger Interactions (STI)
  Sequential Action Interactions (SAI)
  Looping Interactions (LI)
  Missed Trigger Interactions (MTI)
The technique detected all classes except the seven MTIs.
All of the three-way interactions were from the STI class – down to the definitions used!
Rationale : Review : Application : Technique : Results : Conclusions

## Slide 16: Results A Complex Case – Pg. 153
POT 1 : RCI to 2, HL to 2
POT 2 : CFU to 3 and DND
POT 3 : CFBL to 4 and CW
POT 4 : DND and TCS for 1
Eight features on a single call path
Approximately 250 micro-steps along all potential call paths.
Rationale : Review : Application : Technique : Results : Conclusions

## Slide 17: Conclusions Capabilities
Detection of Interactions at a single point of control between an arbitrary number of features, with no internal knowledge of those features
Manual resolution of these interactions with later re-use to provide automation
Extension of techniques to multi-way interaction scenarios
Rationale : Review : Application : Technique : Results : Conclusions

## Slide 18: Conclusions Capabilities - Continued
Classification of interactions into four classes, with different pathologies;
  Shared Triggers : Dangerous, system may behave unpredictably
  Sequential Action : Safe, system is behaving ‘normally’, but stimuli are different
  Looping : Dangerous, A special case of Sequential resulting in busy loops
  Missed Triggers : Dangerous, system may behave unpredictably since it has missed events.
‘Cocooning’ of existing code to allow it’s use without modification in this system.
Rationale : Review : Application : Technique : Results : Conclusions

## Slide 19: Conclusions Limitations and Approaches for addressing them…
Cannot detect MTIs
  Extended feature specifications?
Can only work at a single point of control
  Extensions to network signaling?
Cannot automatically create resolutions to interactions based on rules
  Theoretical study of the trees to see if such automation is possible..
Rationale : Review : Application : Technique : Results : Conclusions

## Slide 20: Some Further Study Areas
Automatic Resolution techniques
Proof of correct operation with legacy systems
Improvement in the loop detection system
MTI detection (resolution?)
Working across multiple points of control (protocols?)
Rationale : Review : Application : Technique : Results : Conclusions