## Slide 1: Home Networks Configuration Management & Service Assurance: Solutions for the 80%
Prepared for: FORCES Colloquium
Glasgow
October 2, 2001
Notes: Opportunity Analysis
For a Network-based Service Activation and Assurance Platform for Home Networking Services

## Slide 2: Overview
Introduction
Why there is a problem, and why it will get worse
  Market Drivers
  Typical elements in a home network.
Architecture to address the issue
Requirements for a solution
Summary

## Slide 3: Sincoskie’s Law
The dominant internet access device changes every six years.
  1984-1990 : minicomputer
  1990-1996 : workstation
  1996-2002 : PC
  2002-2008 : smart cell phone
  2008-2014 : appliance

## Slide 4: But…
Even before we reach this brave new world of network connected appliances, we have a problem…If you have more than one PC in your home (54% of ‘broadband homes’ do), do you know how to configure your network so that they can all;
Access the net?
Play networked games (both client and server)?
Share printers and resources?
Collect and send e-mail?
etc…
….in a secure and reliable fashion?

## Slide 5: A typical home network - 2003
Internet Radio
Broadband Access Termination Device
Broadband Gateway
802.11
NAT Firewall DHCP (client & server)
VPN (PPTP and/or IPsec)
Router
Cable Modem, DSL Modem, Satellite, Etc.
Internet Access Sharing
laptop
Web Terminal
Broadband Access
Service Provider
Network
Access Router
10baseT
10/100baseT
Parallel/USB
service provider services
Internet
PC
Home Domain Boundary
Notes: Telcordia systems and code in red
Broadband Access Termination Device and Broadband Gateway/Router can be co-located in the same physical device.

## Slide 6: Typical Network Elements in 2003…
Broadband access (e.g. DSL modem, cable modem)
Broadband Residential Gateway/Execution Environment (e.g. OSGi)
Multiple PCs with different access constraints and priorities;
  ‘Home’ Machines
  ‘Visitor’ (Friends, work colleagues, etc.)
  ‘Work’ (Different access, VPN connections, etc.)
Printers
Devices with IP-based networking technology
  802.3, 802.11 (WiFi), Home PNA, HomePlug, etc..
A few appliances
  web-pads, digital TVs, smart appliances

## Slide 7: It all has to be configured…
Broadband Gateway/Routers break the end-to-end IP model (due to Firewall and NAT functionality).
  Called a Middle Box in IETF terminology
Many applications (e.g., server-based and peer-to-peer) don’t work with a Middle Box
  Unless the Middle Box and/or applications are specially configured
  For example: Web server hosting, PPTP, IPsec, Multi-player gaming, MP3 file sharing, VoIP (e.g., MS NetMeeting – H.323, SIP), FTP (client-side active), IP-based services (e.g., telnet, FTP, ssh), etc.
Configuring these Middle Boxes is non-trivial.
Configuring end devices (e.g. PCs) is also often required
It’s a mostly mechanistic process, but if I get it wrong it won’t work, it will be difficult to debug, and it might create security holes which users aren’t aware of.

## Slide 8: The solution…let the experts do it!
Average home network user is not equipped to manage network faults or to detect possible performance bottlenecks
  Hard enough to manage a single PC!
Most of it is complicated, rote, management – ideal for a Service Provider to perform.
Also need to be able to detect faults and identify performance bottlenecks remotely
  Provide inputs to the customer for corrective actions
  Or, even better, fix the problem remotely

## Slide 9: Home Network Management
Configuration of:
  Broadband Gateway device capabilities such as firewall, Port forwarding, …
  Configuration of PCs and other end devices
  On-going configuration updates when customer adds services such as VoIP, access to VPNs, …
Fault and performance management issues:
  Firewall mis-configuration
  Availability (e.g., DHCP, DNS)
  Connectivity problems
  QoS performance
  Port forwarding problems
  IP address assignment
  NetBIOS problems
  NAT issues (protocol conversion)
  Multiple DHCP servers
  Multiple DNS servers

## Slide 10: Market Drivers
Deployment of broadband service is costly
  Cost of $700-$1,500 per DSL customer
Service Providers need to increase revenue per customer
  New services
  Home network management customer service offering
Home networks enable many new services
  Sharing Internet access among multiple PCs
  Many more to come (e.g VoIP, multi-player gaming, video)
Deployment of home networks today are impeded by the complexity of managing the devices:
  Initial configuration
  Troubleshooting
  Reconfiguration for each new service or application
54% of broadband households have multiple PCs
70% of DSL customers are interested in home networking

## Slide 11: High Level Architecture
Internet Radio
Broadband Access Termination Device
Broadband Gateway
802.11
NAT Firewall DHCP (client & server)
VPN (PPTP and/or IPsec)
Router
Cable Modem, DSL Modem, Satellite, Etc.
Internet Access Sharing
laptop
Web Terminal
Broadband Access
Service Provider
Network
Access Router
10baseT
10/100baseT
Parallel/USB
service provider services
Internet
PC
Home Domain Boundary
Home Network Manager
agent
agent
agent
agent
Notes: Telcordia systems and code in red
Broadband Access Termination Device and Broadband Gateway/Router can be co-located in the same physical device.

## Slide 12: Why not… What are the advantages to this approach?
Alternatives:
  PC-based
  Gateway-based
Advantages of network-based approach
  Has end-to-end view
  Considers total in-home network (i.e., not just broadband gateway)
  Can correlate faults and performance problems across multiple homes
  Provides easier, automated, administration for the end-user
  Supports flow-through from other systems

## Slide 13: Examples of Services Requiring Configuration Support
Remote Access to corporate network (e.g., PPTP, IPsec)
Web server hosting
Multi-player gaming
MP3 file sharing
Local file sharing
Network printing
Remote access to in-home resources
VoIP (e.g., MS NetMeeting – H.323, SIP)
Firmware upgrade(s)
Security
FTP (client-side active)
IP-based services – e.g., telnet, FTP, ssh
Video Conferencing

## Slide 14: Interfaces to the Network-based System
User
  Web, Cell-phone, Operator
Administrative (Service Provider)
  Web, Integrated with other management systems
Alerting
  User: e-mail, pager, phone-call, IM
  Service provider: e-mail, alarm
Automated
  Flow-through from other systems – e.g., operations systems, service support systems
  Automatic detection of activity in the in-home network

## Slide 15: Fault & Performance Functional Areas
Wide Area Access Functionality
  Firewalls, NATs, Forwarding, Routing
In-Home Networking Services
  NetBIOS (Windows Networking)
In-Home Network Support
  DNS, DHCP, Gateways, IP Allocation etc.
Performance
  LAN-based services, WAN-based services, Access Network
Security Management/Intrusion Detection
  Misconfigured firewalls, intrusion attempts, DoS attacks

## Slide 16: Summary
Home networks are happening now, and the technology we have is not advanced enough to allow my dad to configure it.
People will demand the functionality that home networks can provide, but problems will ensue due to this complexity – mis-operation will be blamed on the network operator!
Network operators need to be able to take proactive role in helping people to configure, manage and monitor their home networks – not for everyone, but as an optional service for the 80% of people who will want the capability, but not the hassle…