## Slide 1
JAIN™: Integrated Network APIs for the Java™ Platform 2nd October, 2001 Phelim O’Doherty JAIN™ Architect Sun Microsystems, Inc. Phelim.ODoherty@sun.com JAINTeam@sun.com http://java.sun.com/products/jain

## Slide 2: The Open API Premise
APIs that are …
  Open
  Industry standard
  Distributed
  Flexible
  Extensible
… will enable an abundance of diverse service offerings to enrich the way we communicate.

## Slide 3: The Promise … Global Market Opportunity
The revenues [for the global softswitch market] will exceed $4.3 billion by 2004.
Yankee Group report, May 2000
By 2003, $14.7 billion of IP solutions and services will be sold.
Piper Jaffray, 1999
In 2002, service providers will invest $795 million in softswitch technology, an investment that will already be cash-flow positive to the tune of more than $1 billion in realized service revenue.
Frost & Sullivan report, 2000

## Slide 4: An Explosion of New Services
Source: US Bancorp Piper Jaffray, Sept 1999
Market size will reach $14.7 Billion in 2003

## Slide 5: Standard Protocols and Open APIs Are the Keys!
“Open, standard APIs hide the complexity of networks from the application layer, and the use of standard signaling and call control protocols are the keys to providing flexibility and creativity for the next-generation networks’ enhanced services.” [Yankee Group]

## Slide 6: JAIN Video
Play >>

## Slide 7: What is JAIN?
JAIN is an enabling set of Java™ APIs to develop and deploy Service Driven network applications and services.
JAIN is an industry framework designed and specified collaboratively by groups of industry partners and experts.
Service Portability - Write Once, Run Anywhere, PROFIT OFTEN
Network Convergence - Any Network
Service Provider Access - By Anyone

## Slide 8: JAIN Community(Spec Lead,Completed Specs)
ADC Newnet
AePONA(GUI)
Alcatel
AT&T
BayPackets
British Telecom
Broadsoft
Cisco
CMG
DataKinetics, Ltd.
Dynamicsoft(SIP/SIP Servlets)
ECTF
Ericsson(MAP)
Eurescom
France Telecom
Fujitsu
Hitachi
Huawei Technologies
Hughes Software(Megaco)
Periphonics
Personeta
Qwest
RADVision(H323)
Samsung
Saraide
Siemens(Mobility)
Sylantro
Sun (TCAP/OAM)
Symsoft
Telcordia Technologies (JCC/MGCP/SCE/JCAT)
TeleSys Software
Teltier Technologies(PAM)
TELSIM-Oxygen Technology
Trillium Digital Systems
TrueTel Communications
Ubiquity Software(SIPLite)
Ulticom(SPA/IM/ISUP)
Westwave Communications
Xybridge
IBM
Incomit
ipVerse
Lara Technology
Logica Mobile Networks
Longboard
Lucent Technologies
Mahindra BT(INAP)
Motorola(SLEE)
Natural Systems
NEC
Net4Call
Netergy Networks
Nokia
Nortel
NTT Comware
NTT Labs
NTT Software
OKI Electric Industry
Open Cloud(NZ)
Panasonic

## Slide 9: JAIN Specifications
JAIN Service Logic Execution Environment (JSLEE)
JAIN Call Control (JCC) and JAIN Coordination and Transactions (JCAT)
JAIN Service Creation Environment (JSCE)
Secure Telco Space
TCAP
ISUP
INAP
SIP
MAP
MGCP
Untrusted third-party applications
JAIN Service Provider Access (JSPA)
Trusted third-party applications
Vendor Independence
Protocol Independence
Network Independence
Operator Independence
Satellite
Security Interface
Megaco
H.323
PSTN
IP
Broadband
Wireless

## Slide 10: JAIN in the Integrated Network
Softswitch
Media Gateways
Signaling Gateway
PSTN
Enterprise
Parlay
Portal
Gatekeeper
Application Servers
JAIN SPA
JAIN SLEE
JAIN JCC/JCAT
JAIN SIP
JAIN ISUP
JAIN INAP
JAIN MAP
JAIN TCAP
JAIN MGCP
JAIN Megaco
User Agents
JAIN H.323
JAIN Megaco
SS7
SIP
MGCP
Megaco
Megaco
H.323
H.323
SIP Servlets
JAIN SCE
SIP
Notes: JAIN is in the network, NOT the transport between the network.
JAIN leaves the protocols to do protocol functions, JAIN is a Java Standard Library that enables service portability and open network access across different protocols and converged networks.
The JAIN API set enables vendors to implement the set of API’s that correlate to their network.

## Slide 11: Why Softswitch?
PROPR I ETARY
Solutions come from a single vendor that supplied everything in one proprietary box: software, hardware and applications
Customers are locked-in to their vendor—no room for innovation, expensive to implement and maintain
Circuit-Switched
Solutions can come from multiple vendors, at all levels who supply open standards-based products
Customers are free to choose best-in-class products to build their network. Open standards enable innovation and reduce costs
Soft-Switched
Transport Hardware
Softswitch Call Control
Services, Applications & Features (Management, Provisioning and Back Office)
Open Applications APIs
Open Protocols APIs
Transport Hardware
Call Control & Switching
Services & Applications

## Slide 12: Benefits of a Softswitch
Improved services
  New services, integration with existing networks, “convergence”
Facilitate migration to IP networks
Reduced Costs

## Slide 13: JAIN in the Softswitch
Softswitch
Media / Signaling Gateways
Gatekeepers
JAIN JCC/JCAT
JAIN MGCP
JAIN Megaco
User Agents
JAIN H.323
SIP
MGCP
H.323
H.323
SIP
MGCP
Megaco
or
Megaco
JAIN SIP
JAIN Megaco
JAIN MGCP
JAIN SIP
JAIN H.323
Notes: The JAIN API’s are two-fold in that they support endpoints and are also dominant in the core of the network
JAIN JCC and JCAT are abstractions that enables portable services that are protocol independent.
The other JAIN API’s provide functionality for Applications that require extensive knowledge of the underlying protocol.

## Slide 14: What is Java Call Control (JCC)?
JCC is the Java realization of a simplified version of Parlays MPCCS.
JCC aligns with both Parlay MPCCS and JTAPI.
JCC is based on AIN/IN experience, but is protocol agnostic.
JCC is out there and available!
Notes: The JAIN API’s are two-fold in that they support endpoints and are also dominant in the core of the network
JAIN JCC and JCAT are abstractions that enables portable services that are protocol independent.
The other JAIN API’s provide functionality for Applications that require extensive knowledge of the underlying protocol.

## Slide 15: The Beginning: Many Call Models
JTAPI
Extensions
JTAPI
Core
CTI space
Java Call
Control
(JCC)
Java Coordination & Transactions
(JCAT)
NSP space
Parlay CC
3rd Party space
3GPP
CN5
Mobility space
ITU-T SG11
IN+IP space
ETSI SPAN3
IN space
Notes: Services and Protocols for Advanced Networks (SPAN)
SPAN3
Competence Centre for IN (formerly SPS3)
Activities
IN Protocol Design and Interfaces (Core INAP)
Transaction Capabilities (TCAP)
Inter-working aspects for IN /UNI; IN / NNI : includes the Production of a living document by working group SPAN3 and delivered to working groups SPAN1 & SPAN5 .
Generic Operations for INAP Mobility (e.g. CAMEL, CTM, etc.)
INAP Test Specifications
Interaction aspects of INAP and applications using IP

## Slide 16: Goal: A Family of Call Models
Java Call
Control
(JCC)
Java Call
Processing
(JCP)
JAIN space
Java Coordination & Transactions
(JCAT)
3rd Party space
Parlay
Extensions
3GPP
Extensions
Mobility space
Based on
Parlay 2.1
MPCCS
JTAPI
Extensions
JTAPI
Core
CTI space

## Slide 17: JAIN Call Control (JCC) API
Call control: observing, initiating, answering, processing and manipulating “calls”
JCC = unified call control for multimedia, multiparty, multiprotocol sessions over underlying integrated networks
Simple yet provides a reasonably rich set of functions
Support first-party as well as third-party calls
Complex and special cases to be handled by extensions (e.g. JCAT, User Interaction)
Example service drivers:800/900 Number Translation, Wake-up Call, Voice Activated Dialing, Click to Dial
Copyright ©2001 Telcordia Technologies. All Rights Reserved.

## Slide 18: Basic JCC approach
Application
Call
Provider
Connection
Connection
Call
Listener
Connection
Listener
Provider
Listener
Synchronous
method calls
Java
Events
JCC API
Network
JAIN and Parlay Terminology Map: Provider = Call Control Manager
Connection = Call Leg
Copyright ©2001 Telcordia Technologies. All Rights Reserved.

## Slide 19: Click-to-Dial Example using JCC
Click-to-Dial
server application
GW
GW
CTD user (#1001)
Called party
(#2001)
Softswitch
JCC API
Click-to-Dial
client application
WWW
browser
WWW
server
(2) App
verifiesCTD user (by IP address)
(3) App requests CA to set up
call between #1001 and #2001
(4) CA rings #1001
(5) When #1001 has answered, CA alerts #2001
(6) When #2001 has answered, CA
completes call from #1001 to #2001
Database of CTD
users - Profiles
Copyright ©2001 Telcordia Technologies. All Rights Reserved.
(1) CTD requests
call to #2001

## Slide 20: Industry Alignment
Joint Call Control,
Mobility, User Interaction
ETSI ES 120070
& ES 120075 (parts 1-12)
ETSI
SPAN3
3GPP
OSA
JAIN
Parlay
120070 = API for Open Service Provisioning
120075 = API Mapping for Open Service Provisioning
Notes: [Richard Stretch’s Notes]
At the last Parlay meeting, members of ETSI and 3GPP were invited to sit down and work out some sort of process that would facilitate this goal.
It was decided that the ETSI process and in a way control of the specification was the best means of ensuring that IPR and NDA issues do not cloud the proceedings and enable the group to get going without getting embroiled in Politics and legal wrangles.
The Parlay meeting decided that it would be best if this new joint group considered not only call control but also Mobility and User interaction, as these two other interfaces may have a direct impact on Call Control.
Now ETSI/Parlay had already provided what is widely known as Version 2.1. It was clear that this model needed some adjustments to it to capture the needs of the Java/JAIN Call Control API.
As this would be an ETSI process it was decided to use the draft standard 120070 as basis for the work as this contained all of the Parlay 2.1 and 3GPP release ‘99 requirements. The goal is to enhance this to a 2.2 spec capturing JAIN’s needs.
[My additional notes]
The end result of these technical negotiations is expected to be one unified call control model for the industry. The resulting API specifications will filter back to each of the relevant groups, and new aligned versions of their respective call control APIs will emerge.

## Slide 21
NTT Network Service Systems Laboratories © NTT 2001
Application Portability across NGN-CAs using JAINTM
High-speed Broadband Internet Backbone
NGN-CA
(NEC)
Open API
Platform
APL
NGN-CA
(Fujitsu/Lucent)
Open API
Platform
APL
Application
Software
(NTT)
JAINTM
Call Control
APIs
・・・・・・・・・・・・
・・・
Broadband
Internet Access
Dialup,Mobile
High-Speed Broadband
Internet Access
JAINTM
Call Control
APIs
NGN-CA realizes
the efficient development and deployment of new services
and stimulate the network service market.
Notes: <number>
<footer>
<header>
<date/time>
Up to now, the approach to develop applications independently of the network platform has been to define APIs, or Application Programming Interfaces between applications and the platform. For the next-generation network, this approach is being extended in the form of open APIs expected to enable application use across heterogeneous platforms. JAIN, using Java technology for rapid application development, is an especially promising candidate as open APIs in the next-generation network of integrated data and stream services.
NTT, with collaborative efforts of NEC, Fujitsu and Lucent technologies, has developed JAIN Call Control or JCC platform and succeeded in porting application software among heterogeneous Control Agents. It was the world’s first successful verification of application portability over JCC.
NGN-CA realizes the efficient development and deployment of new services and will stimulate the network service market.
Please visit NTT booth and see their demonstration and also the JAIN time ! Ms.Margaret and Mr.Steven will introduce the JAIN activities at NTT booth!

## Slide 22: Where to Find JCC
JCC 1.0 API (First Public Release) available at SUN site:
http://jcp.org/jsr/tech/jain.jsp
JCC 1.0 RI and TCK are available at Telcordia site: http://www.argreenhouse.com/JAINRefCode/

## Slide 23: SIP Everywhere….
MGC’s/SIP Proxies
Application Servers
Endpoints
IP / ATM
MGC’s/SIP Proxies
Application Servers
IP / ATM
MGC’s/SIP Proxies
IP / ATM
Different types of
SIP Applications
requiring different
Abstractions of the SIP API.
Notes: SIP is everywhere in the network, different types of Applications run in different parts of the network, therefore different abstractions of the SIP protocol are required in different parts of the network.
JAIN Addresses this!

## Slide 24: JAIN in the SIP Network
Directory Servers
Email Servers
Media Servers
Web Servers
Application Server
User Agents
Proxy / Redirect Server
SIP
SIP
SIP
SIP
SIP
Packet Network
Packet Network
SIP
SIP Servlets
SIP Lite
JAIN SIP
SIP Lite
SIP Lite
JAIN SIP
JAIN SIP
JAIN SIP
SIP Servlets
Notes: JAIN SIP is targeted at the User Agent and at the Proxy servers
JAIN SIPLite is focused mainly on the User Agent or back to back User Agents to enable 3rd Party call control
SIP Servlets are web based and targeted at the Proxy and Application servers.

## Slide 25: JAIN in the SIP Stack
Session Layer
SIP
Packet Network
Message Layer
Raw API
Abstract API
SIP Servlets
JAIN SIP-Lite
Transaction Layer
JAIN SIP v1.0
Notes: See upcoming slides

## Slide 26: JAIN and SIP
JAIN SIP v1.0
  Exposes all functionality in the SIP Protocol
  Defines complete set of messages headers and bodies within the protocol as Interfaces
  Notation of SIP messages associated by transactions, based on the JavaBean Event model
  Targeted at low level stack applications that require exposure to complete SIP protocol
  Public Domain Implementation available:
      http://www.antd.nist.gov/proj/iptel

## Slide 27: JAIN SIPv1.0 Architecture
Proprietary SIP Stack
Setup Function
JAIN IP Factory
createStack()
createProvider()
getInstance()
Event
Registration
createListener()
JAIN SIP Stack
JAIN SIP Provider
JAIN SIP
Listener

## Slide 28: JAIN and SIP
JAIN SIPLite
  Notation of SIP sessions upon which high level messages are sent – based on JavaBean Event Model
  Implementation must create messages, shielding the lower workings of the protocol away from the application
  Abstracts away from message definition by defining simple message types upon which SIP messages can be created
  Restricted functionality, however is focused for simple applications

## Slide 29: JAIN and SIP
JAIN SIP Servlets
  SIP servlets will typically reside on network servers where they will be responsible for making routing decisions.
  Utilizes http servlet model as foundation, builds on http generic part for essential SIP request and response functionality
  Notation of SIP Sessions that are the equivalent of call legs, that include a collection of calls

## Slide 30: JAIN and Parlay
The JAIN Service Provider APIs define a full industry standard Java technology realization of the Parlay APIs:
  Complete Java specifications
  Java Reference Implementations
  Technology Compatibility Kit (i.e., Java test suite)
  Auditing and Certification program
The Java/JAIN and Parlay Communities -- A Winning Team !!

## Slide 31: Parlay in the Network
Network
Security
Boundary
The Parlay APIs
Network
Elements
Enterprise
Domain
Service
Provider
Domain
SCP
Internet
Managed IP
Network
Network
Elements
Mobile
Network
Hosted Application
Server
Application
Server
Router
HLR
Parlay Applications
Intranet
Fire
wall
Parlay
Gateway
Parlay
Gateway
PSTN
Network
Elements
Notes: Typical Network Service Provider end-to-end solutions consist of 5 components in 4 layers:
The Network Layer, comprising the core bearer, switching, trunking, (media) gateway and policy enforcement equipment, accessible and visible by the call processing platform through Network Protocol Stacks,
The Signaling Layer, managing the network layer by handling aspects such as call setup and teardown, (media) gateway, multiplexer and transcoding control, policy deployment and generation of service triggers,
The Services Layer, holding the communication service logic (and associated provisioning),
The service layer typical consists of a Service Creation Environment and a logic Execution Environment, and
The Back Office Functionality, e.g. provisioning, billing, customer support and management.

## Slide 32: Parlay Architecture The Parlay View
Parlay
Server/Gateway
Application Servers
(Parlay clients)
Network Protocol Stacks, e.g.
ISUP, TCAP, SIP, MGCP, H.323
Secure interface.
Parlay defined in UML
and mapped to IDL
Internet

## Slide 33: JAIN based Parlay Case Study JAIN building blocks
e.g. IIOP
Services
JAIN SPA
Parlay Client
APIs
APIs
Standard
Java
API
APIs
Parlay Server
Parlay
FW
Parlay
CC
Parlay
Mob
JAIN
MAP
JAIN
SIP
JAIN
INAP
Std
Java
API
JAIN Protocol APIs
JAIN SPA APIs

## Slide 34: Why JAIN Protocol APIs in a Parlay Implementation?
Stack vendor independent
  Stack vendor can focus on stack performance and scalability
Simple and similar API Architecture for all protocol APIs
  Shortens learning/development time when adding support for new protocols
  Easy to move from one API to another

## Slide 35
JAIN ”Protocol” APIs Architecture
Parameter
Factory
Exception
Misc
Listener
Listener Interface
Proprietary Protocol Stack
Stack Interface
Stack
Provider Interface
Provider
Primitive
JAIN Protocol API

## Slide 36: JAIN Service Provider API (SPA)
SPA APIs
  SPA Framework APIs
    Trust and Security Management
  Generic User Interaction
  Mobility
  Call Control (JCC)
e.g. IIOP
Services
JAIN SPA
Parlay Client
Standard
Java
API
Parlay Server
Java technology mapping of Parlay/OSA specifications
Non FW APIs can be used stand-alone
JAIN SPA implementation is not necessarily built on top of Parlay

## Slide 37
NTT Network Service Systems Laboratories © NTT 2001
High-speed Broadband Internet Backbone
NGN-CA（ Control Agent for Next Generation Network
NGN-CA
Open API
Platform
Open API
NTT
3rd
vendor
APL
APL
ASP
NGN-CA
RADIUS
WWW
LDAP
・・・
・・・
Deployment
Service
Supply
APL
SA
・・・・・・・・・・・・
・・・
Broadband
Internet Access
Dialup,Mobile
High-Speed Broadband
Internet Access
APL
APL
(JAINTM, Parlay)
Notes: <number>
<footer>
<header>
<date/time>
The NTT Network Service Systems Laboratories have been studying the Control Agent or CA, a solution for the next generation network, in collaboration with NEC, Fujitsu and Lucent Technologies. Inc. through NTT’s RFP, Request For Proposal which is the international procurement procedure.
This NGN-CA, Control Agent for Next Generation Network
enables not only NTT but ISVs or ASPs to take advantages of Carrier Network Functions and deploy their own new services
through Open API such as JAIN and Parlay.

## Slide 38: THANKS!!
Questions?
?
?
?
?
?
?
?
?
?
?