## Slide 1: The Parlay API
Ivan Boyd
Advanced Communications Research, BT, Adastral Park

## Slide 2: Old Telecommunications World
Intelligence
Dumb Terminals
communication trends

## Slide 3
The Internet
Servers
communication trends

## Slide 4
The Internet
Servers
Intelligence Migration
from Central Network
toward Edge-of-Network
communication trends

## Slide 5
Telco World Today
Physical Networks
Service Components
Applications

## Slide 6
Telco World Today
ISDN, PSTN, IP...
Authentication, Routing,
Billing, Storage, Configuration...
800, Personal Numbering
Voice messaging...

## Slide 7
Telco World Today
ISDN, PSTN, IP...
Authentication, Routing,
Billing, Storage, Configuration...
800, Personal Numbering
Voice messaging...
Owned and Operated
by the Telco

## Slide 8: Concept
The Telco World of
Networks and Services
API

## Slide 9
API
Service Components
1
2
3
n
Physical Networks
Network Operator
End User domain
Application / SP
domain
{
Applications

## Slide 10: Move from all Telco owned to….
ISDN, PSTN, IP...
Authentication, Routing,
Billing, Storage, Configuration...
800, Personal Numbering
Voice messaging...
Owned and Operated
by the Telco
The Telco World
Rich in Networks
API
The IT World
Rich in Applications
Convergence

## Slide 11
The Parlay Group (http://www.parlay.org)

## Slide 12: The Project - History
Started - March 1998
5 Company, Cross Industry Group
  BT
  Microsoft
  Nortel Networks
  Siemens
  Ulticom
Phase 1 Specification and Demo - Dec 98
  Open, Technology Independent, Secure, Communication Services Network API

## Slide 13: API Characteristics
Object oriented
Multi-Media (not just telephony)
Manageable
Secure
Simple (easy to use)
Extensible (functional, mgmt, billing)
Multiple Networks
Notes: Object Oriented (adopted as it is an efficient and proven approach to specifying APIs)
Multi-media (the API will support services with different media types, not just telephony)
Manageable (essential characteristic if network operators are going to deploy the API)
Secure (unless both service providers and network operators are convinced that the security of their respective domains is maintained the API will never be adopted by the industry)
Simple (essential that the API is easy to use or applications developers will not employ it)
Extensible (the aim of the Parlay Group is to expand the API in a series of phases and hence extensibility of both the service and management support functionality is essential)
  Supports Discovery (a capability that enables the application developer to request a ‘logical’ capability leaving the API to locate a particular interface to perform the requested operation)
Network Independent (enterprise applications can operate across multiple network technologies)
Affects Call Before ‘Delivered’, reducing cost and resource utilization (this is in contrast to enterprise CTI where calls are delivered to the edge of the network, where they may be processed and then be re-directed ‘tromboning’ through part of the network)
Global in Scope - Provides abstracted common services that work the same way on different networks, technologies, and countries.
E-Business Oriented - Allows creation of multiple (nested) service delivery and billing tiers

## Slide 14: API Technical View
Framework Interface Set - Common Functions That Are Required to Enable Services to Work Together in a Coherent Fashion
Service Interface Set - Common Functions That Deliver Whole Complex Services or Sub-components of Services (Micro Services)
Notes: The Parlay API consists of two categories of interface:
Service Interfaces. These offer applications access to a range of network capabilities and information.
Framework Interfaces. These provide the supporting capabilities necessary for the Service Interfaces to be secure, resilient, located and managed.
Examples of the supporting functionality provided via the framework interfaces are listed below. These examples are taken from the version 1.1 Parlay framework interface:
  Authentication
  Discovery
  Event Notification
  Integrity Management
  Operation, Administration, and Maintenance

## Slide 15: Architectural View
Notes: The architecture of the Parlay API is illustrated above. This figure illustrates the relationship between applications, the framework and service interfaces, resource interfaces (see below) and networked equipment.
Resources
  Network Functionality
Resource Interfaces
  Intra-network Control of Resources
Framework and Service Interfaces
  Parlay API Elements As Described Earlier
Applications
  Extra-network Logic, Data and Resources

## Slide 16
Network
Elements
Service
Application
Network
Access to Sensitive
Data (e.g. routing plans)
from the network or
other service providers
Fraudulent use
of network resources
Attempts To Deny
Service To Valid Users
Unauthorized
Modification
of Network
Invocations
Access to Sensitive
Data (e.g. billing data)
from outside the network
Security Threats

## Slide 17
API Security Model Defence In Depth
Network
Elements
API
Service
Application
Firewall
Gateway /
Converter
Gateway /
Converter
Authorization
Server

## Slide 18
API Security Model Futures
Network
Elements
Gateway /
Converter
API
Firewall
Authorization
Server
Service
Application
Audit
Intrusion
Management

## Slide 19: Call Control and Messaging
Phase 1 enables
Notification of incoming calls / events
Establishing of call legs and connection
Status of call (ringing, hang-up, etc)
Process user dialled digits and caller line identity (CLI)
Control of voice and e-mail messaging functions

## Slide 20
Parlay Demonstration
Dr Nicholas Edwards Business Technology Analysis Unit, BT

## Slide 21: The BT Parlay Testbed
Gateway (C++)
Telephone
Network
PARLAY
APPLICATION
DCOM, CORBA
Application (C++, VB)
Telephones
ISDN30
Notes: <number>
<footer>
<header>
<date/time>
At the heart of the system is a central messaging and control centre. Here there is a computer database with information on everyone who is being monitored.
On a regular basis - say once an hour - the control centre sends a telephone call to each home. The system uses a special type of telephone call which does not cause the person’s telephone to ring, but allows the lifestyle information to be retrieved from the home.
Thus a database is built up of a person’s lifestyle patterns.

## Slide 22
Call Routing
Parlay API
User
Interfaces
Generic Call Router Application
Gateway
Telephone
Network
Rules

## Slide 23: FriendsLink Logic
Incoming call
Social hours
Destination
Answered?
Out-of-hours
Not answered
No
Yes
Time-of-Day?
Family or friend?
Callminder

## Slide 25
MultiRing
Incoming call
Office
No
Factory Floor
Yes
Important customer?
Not answered?
First to answer?
Callminder
Connect

## Slide 27: What’s New in the Phase 2 API ?

## Slide 28: The Project - Phase 2
Started - May 1999
Expanded Membership
  AT&T
  BT
  Cegetel
  Cisco
  Ericsson
  IBM
Phase 2 Activities
  Expand Specifications with Focus on Wireless and IP
  Release Specification with Demo - January and February 2000, UK and US
  Lucent
  Microsoft
  Nortel Networks
  Siemens
  Ulticom (formerly DGM&S Telecom)
NEW
NEW
NEW
NEW
NEW
NEW

## Slide 29: New Service Interfaces
Mobility Management
  General location & positioning functions for fixed, mobile & IP-based networks
  User status: reachable, not reachable
IP Connectivity Management
  Provisioned Quality of Service (QoS)

## Slide 30: New Framework Interfaces
Auditing
  Audit file management functions
  Usage Data Storage
Integrity Management
  Load balancing functions for the whole API and generic load balancing for services
  Fault management functions for the whole API and generic fault management for services

## Slide 31: Telecom Services Today Look a Lot Like Mainframe Apps of the Glass House Era
  Services Focused on the Mass Market
  Tightly Controlled by a Few Vendors
  Long Creation and Deployment Times
Parlay is Changing the Paradigm !
  Portable Services - Created Quickly
  Created by any software developer, for Enterprises, service providers and network operators