## Slide 1: Next Generation Networks (NGNs) - what they are and what it means
© 1999 Telcordia Technologies - All rights Reserved.
Prepared For:
The FORum for the Creation and Engineering of Services (FORCES)
Telcordia Contact: Dave Marples
Senior Scientist
(973) 829 2375
July 30, 2026
An SAIC Company

## Slide 2: Introduction
What is a NGN anyway?
Prove that IP-based telephony works
Discussion of today's telephony networks
How that’s going to change over the next few years
Why this change will happen
What this change means for consumers
How to take advantage of it
Conclusions

## Slide 3: The Phone Call I just made...
PC Client
Laptop
PC Client
Laptop
PC Client
Etherphone
PSTN
877-699-NGN1
Mobile Phone
Landline
AS5300
AS5300
PC Client
Etherphone
NetMeeting
NetMeeting
NetMeeting
NetMeeting
PSTN
732-699-6461
Phone
Centrex
5ESS
AIN
Voice Over IP
Telcordia
SAIC
4700
Cisco1400
7513
7513
6Mb
6Mb
1.5Mb
DL3800 IMUX
DL3800 IMUX
Frame Relay
Phone
PSTN
PBX
Lucent
PRI
PRI
Gateway
Gateway

## Slide 4: What is an NGN?
A network based on new technology to solve communications needs
An integrated (converged) network covering voice, data and multimedia requirements
An evolutionary step from today's network implementations
Equally applicable to wide area (WAN, Public) and local area (LAN, Private Network) communications
A cheaper way of communicating, using IP instead of switched circuits

## Slide 5: Let’s dispel some myths….
IP Telephony is poor quality, with delays and dropouts. No, it’s toll quality. You can’t tell the difference.
IP Telephony is unreliable, built on PCs and other ‘consumer grade’ hardware. No, its 99.999 reliability, on fault tolerant high availability systems.
IP Telephony is expensive, and it’s difficult to implement and administer. It’s cheaper to maintain one infrastructure than two, and staff are already trained in most of the appropriate technologies.
IP Telephony is a future technology. No, it’s here now and it works.

## Slide 6: How IP Telephony is carried
Media are carried in Real Time Protocol (RTP) with Real Time Control Protocol (RTCP) support.
Network is either over-engineered or supports QoS management.
But, carrying the media is only one part...
IP Cloud

## Slide 7: Call Control
Needed to route calls between endpoints, not to mention billing, authentication and features.
Devolves functionality from the endpoints and places it into a server capability.
IP Cloud
Call
Control

## Slide 8: Control and Bearers
IP Cloud
Call
Control
SGCP/MGCP/
SIP/H.323
RTP/RTCP

## Slide 9: Potential Call Control Points
IP Cloud
Call
Control
PC Client
AIN
Parlay
TAPI
Feature
Phone
Switch-based
Functionality
Third
Party
Apps
Local
Capabilities

## Slide 10: Establishing a Call...
Off Hook
Collect digits
Dialled Digits
Incoming Call from A
Voice Bearer
Ringing Out
Answer
Establish forward Bearer
Voice Call
Digits
Dialtone
Off
Hook
Call Agent
RGW A
RGW B

## Slide 11: The Telcordia NGN Solution
TCAP/SS7
ISUP/SS7
MGCP
MGCP
SS7
Gateway
Public Signaling Network
ISCP
Customer
Care &
Billing
Network
OSSs
MGCP
Service
Definition and
Execution
Customer
TelCo
Service Applets
- Service Definition - Billing - Provisioning
GUI
JAVA
Trunking
Gateway
Backbone
Network
Res Hub
Voice/IP
Voice/IP/ATM
SONET
Call Agent
Exchange
Link
HFC
ADSL
WLL
Annc
Server
ISP
TCAP/SS7
Service
Programs
PSTN

## Slide 12: Real, Public, Implementations
Call Agent
IN
MGCP
Packet Network
Applications
Expense
Revenue
PSTN
Sprint ION Network
Videotron

## Slide 13: What does this mean?
Switches will go from being large, monolithic creatures with collocated connection and bearer control to distributed, IP-centric systems.
We should reasonably expect this to happen first with emergent carriers rather than established ones.
The power of an IP infrastructure will be leveraged to create features in many different, non-traditional environments. The power of a converged infrastructure will lead to the development of many new services.
The cost of infrastructure will go down as telecommunications moves out of its own small independent world to take advantage of the benefits of scale in the data world.

## Slide 14: Why?
Convergence - it’s no longer sufficient to be a telephony provider, you have to be a communications services provider.
Cost reduction - one infrastructure is cheaper than two, and an IP infrastructure is cheaper than a SS7 one.
Flexibility - VPNs, cross-switch systems.
Migration - Ability to build on current infrastructure.
Versatility - why should a phone call be a 3.1kHz, mono audio channel?
Scalability - Grow your network to meet demand.

## Slide 15: Changes for customers
Emergence of non-traditional telecomm carriers - cable companies being the first group.
Enhanced features - since systems are IP-centric, ‘net-friendly’ features will quickly be deployed.
Cost reductions due to increases in competition.
Decrease in distance-related toll loading.
Move away from Telephony as distinct from general connected computing.

## Slide 16: Enterprise Adoption of NGN/IP Telephony
Low capital cost - can be introduced incrementally
Remote/Branch office integration via cheaper technologies - simplified topology, management and security infrastructures.
Consolidation of voice and data on a single wire (50-60% cost savings)
Single infrastructure - cost savings in implementation and ongoing maintenance.

## Slide 17: Will it happen?
By 2003, 70% of enterprises will have replaced at least 2/3 of their networks and 15% will have replaced their networks totally (0.7 probability)
Starting in late 1999, enterprises will test integrated voice and data alternatives, but less than 20% will use the technology by 2001 (0.7 probability)
By 2003, more than 50% of intra-enterprise communications needs (including voice) will move from individually procured network services to a converged, multiservice network-service provider (NSP) network (0.8 probability) Key strategic planning assumptions from; “Networking Battlefield: How to Profit From a Once-in-a-Lifetime Opportunity,” Gartner Group, August 17, 1999

## Slide 18: The future for Telcordia...
Call Agent Plus
VPNS
SDX PBX
Aberdeen, UK
SDX PBX
Maidenhead, UK
SDX PBX
London , UK
VPNS
Hubbing
5ESS Centrex
Morristown, NJ
5ESS Centrex
Navesink,NJ
Frame Relay
Nortel PBX
McLean, VA
Lucent PBX
San Diego
5ESS Centrex
Piscataway, NJ
NEC PBX
Lisle, Ill
Call Agent Plus
Accounting Gateway
Announcement Server
Billing System
Performance / SNMP
Corporate Directory
Routing Management

## Slide 19
An SAIC Company