## Slide 1: Handling Incompatibilities between Services deployed on IP-based Networks
Mario Kolberg
University of Stirling
mko@cs.stir.ac.uk

## Slide 2: Contents
Internet Telephony
Overview of SIP
Services in SIP
Feature Interactions in SIP
Overview of the proposed Approach
Results
Conclusions

## Slide 3: Motivation for Internet Telephony
cheap phone calls
integrating traditional voice services with Internet services
call may include video, text chat, etc
separate network and service provisioning
third party service provisioning
create services for a small number of users
user create their own services
Internet telephony offers rich signalling
intelligent end devices
separation of signalling and contents data

## Slide 4: Protocols for VoIP
strong connection between the protocols used and programming VoIP services
Signalling Protocols
  SIP (Session Initiation Protocol)
  H.323
  MGCP (Media Gateway Control Protocol)
Description Protocols
  SDP (Session Description Protocol)
Transport protocols:
  RTP (Real-time Transport Protocol)
  RSVP (Resource Reservation Protocol) for QoS

## Slide 5: SIP
SIP is a protocol for initiating, modifying and terminating interactive sessions
  is explicitly distributed with local user control
  enables creation and sharing of information
supports existing telephony features but is also designed for new applications enabled by the Internet
  highly personalised call control
  lightweight and extendible

## Slide 6: SIP Architecture
Components
  User Agents
  statefull and stateless Proxy-Servers
  Redirect Server
  Register Server
Stateful Proxy
Redirect Server
Stateless Proxy
INVITE
INVITE
INVITE
INVITE
302
ACK
MEDIA PATH
200 OK
200 OK
200 OK
ACK
ACK
ACK
SIP PATH
User Agent Server
Callee
User Agent Client
Caller

## Slide 7: SIP Messages
either Request or Response
can be passed between UA and UA, UA and Server, Server and Server
contains Request-Line, Header, Message
Status Codes
1xx Informational: - Trying - Ringing - Being Forwarded - Queued
200 Success
3xx Redirect
4xx Client Error
5xx Server Error
6xx Global Error
INVITE ACK OPTIONS BYE REGISTER CANCEL
NOTIFY SUBSCRIBE REFER

## Slide 8: INVITE
INVITE
INVITE sip:dave@falcon.telcordia.com SIP/2.0 Via: SIP/2.0/UDP sip.cs.stir.ac.uk Via: SIP/2.0/UDP sip.telcordia.com To: sip:dave@telcordia.com From: sip:mko@cs.stir.ac.uk Contact: sip:mko@eagle.cs.stir.ac.uk Call-ID: 123456@3.4.5.6 `CSeq: 1 INVITE
sip:mko@eagle.cs.stir.ac.uk
sip.cs.stir.ac.uk (stateful proxy)
sip:dave@falcon.telcordia.com
sip.telcordia.com (stateful proxy)
UAC
UAS
INVITE
INVITE sip:dave@telcordia.com SIP/2.0 Via: SIP/UDP/2.0 sip.cs.stir.ac.uk To: sip:dave@telcordia.com From: sip:mko@cs.stir.ac.uk Contact: sip:mko@eagle.cs.stir.ac.uk Call-ID: 123456@3.4.5.6 CSeq: 1 INVITE
INVITE
INVITE sip:dave@telcordia.com SIP/2.0 Via: SIP/UDP/2.0 sip.cs.stir.ac.uk Via: SIP/UDP/2.0 sip.telcordia.com To: sip:dave@telcordia.com From: sip:mko@cs.stir.ac.uk Contact: sip:mko@eagle.cs.stir.ac.uk Call-ID: 123456@3.4.5.6 CSeq: 1 INVITE

## Slide 9: Responses
sip.cs.stir.ac.uk (stateful proxy)
sip:dave@falcon.telcordia.com
sip.telcordia.com (stateful proxy)
UAC
UAS
200 OK
SIP/2.0 200 OK Via: SIP/2.0/UDP sip.cs.stir.ac.uk Via: SIP/2.0/UDP sip.telcordia.com To: sip:dave@telcordia.com From: sip:mko@cs.stir.ac.uk Contact: sip:dave@falcon.telcordia.com Call-ID: 123456@3.4.5.6 CSeq: 1 INVITE
200 OK
200 OK
sip:mko@eagle.cs.stir.ac.uk
ACK
ACK sip:dave@falcon.telcordia.com Via: SIP/2.0/UDP sip.cs.stir.ac.uk Via: SIP/2.0/UDP sip.telcordia.com To: sip:dave@telcordia.com From: sip:mko@cs.stir.ac.uk Contact: sip:mko@eagle.cs.stir.ac.uk Call-ID: 123456@3.4.5.6 CSeq: 1 ACK
ACK
ACK

## Slide 10: Tier down
sip.cs.stir.ac.uk (stateful proxy)
sip:dave@falcon.telcordia.com
sip.telcordia.com (stateful proxy)
UAC
UAS
BYE
BYE sip:mko@eagle.cs.stir.ac.uk Via: SIP/2.0/UDP sip.cs.stir.ac.uk Via: SIP/2.0/UDP sip.telcordia.com To: sip:mko@cs.stir.ac.uk From: sip:dave@telcordia.com Contact: sip:dave@falcon.telcordia.com Call-ID: 123456@3.4.5.6 CSeq: 2 BYE
BYE
BYE
sip:mko@eagle.cs.stir.ac.uk

## Slide 11: Options
sip.cs.stir.ac.uk (stateful proxy)
sip:dave@falcon.telcordia.com
sip.telcordia.com (stateful proxy)
UAC
UAS
200 OK
SIP/2.0 200 OK Via: SIP/2.0/UDP sip.cs.stir.ac.uk Via: SIP/2.0/UDP sip.telcordia.com To: sip:dave@telcordia.com From: sip:mko@cs.stir.ac.uk Call-ID: 5675@3.4.5.6 CSeq: 1 OPTIONS Allow: INVITE,ACK,OPTIONS,CANCEL,REFER Accept: application/sdp;level=1, text/html Accept-Language: da, en-gb,q=0.8, en;q=0.7
200 OK
200 OK
OPTIONS
OPTIONS sip:dave@telcordia.com Via: SIP/2.0/UDP sip.cs.stir.ac.uk Via: SIP/2.0/UDP sip.telcordia.com To: sip:dave@telcordia.com From: sip:mko@cs.stir.ac.uk Call-ID: 5675@3.4.5.6 CSeq: 1 OPTIONS
OPTIONS
OPTIONS
sip:mko@eagle.cs.stir.ac.uk

## Slide 12: Register
UAC
registrar.cs.stir.ac.uk
(Register Server)
sip.cs.stir.ac.uk
stateful proxy)
Location Server
REGISTER
200 OK
sip:mko@eagle.cs.stir.ac.uk
SIP/2.0 200 OK
To: sip:mko@cs.stir.ac.uk From: sip:mko@cs.stir.ac.uk CSeq: 1 REGISTER Contact: sip:mko@eagle.cs.stir.ac.uk&expires=12:00 Call-ID: 1234
REGISTER:sip:registrar.cs.stir.ac.uk SIP/2.0
To: sip:mko@cs.stir.ac.uk From: sip:mko@cs.stir.ac.uk CSeq: 1 REGISTER Contact: sip:mko@eagle.cs.stir.ac.uk&expires=12:00 Call-ID: 1234

## Slide 13: Services in SIP
SIP Server
Function
Service Logic
Programming Interface
Requests
Requests
Responses
Responses
SIP-CGI (Trusted Parties, e.g. Administrators)
CPL (Un-trusted Parties, e.g. End-Users)

## Slide 14: CPL
Guaranteed to complete: No loops. No recursion.
Safe to execute: Restrained environment.
Standardized Representation:
Readable and Producible: human or machine.
Protocol Independent:
  Independent of Operating System or Signaling Protocol
Ease of Transport: File representation.
Interpreter can manage the conditions.

## Slide 15: CPL cont …
A Language used to describe and control Internet Telephony Services.
Designed to be implemented on either Network Servers or User Agent Servers.
Describes Services as a Decision Graph based on XML Syntax.
Condition
Action 1
Action 2
True
False
Succeeded
Failed
Outcome 1
Outcome 2

## Slide 16: CPL Features
Script Creation by End Users (Customized call filtering)
Third Party Outsourcing
Administrator Service Definition (Define enterprise policies)
Web Middleware
  Service creation and customisation using WEB interfaces.
In a Signalling Server controls proxy, redirect, or rejection actions for the set-up of a call.
Focused on “local” control rather than “global” coordination of multiple signalling servers as in IN
Defines a list of Condition/Action Pairs that concentrates on user “location” routing.

## Slide 17: SIP-CGI
Language Independence (Perl, C, etc)
Creation of all aspects of a response
Access to any resource (flexible interface)
component reuse (reuse of HTTP-CGI)
environment familiarity
easy extensibility
invoked when a request arrives at the server
result of the script specifies the servers actions
persistent (script can also handle responses to generated requests)

## Slide 18: Feature Interactions in SIP
The problem is not going to go away in SIP!
Some Examples
  Forking + Voicemail
  ‘Camp on’ + Call Forwarding Busy
  traditional interactions (MUMC, OCS+CFU)
Good News: Services may communicate

## Slide 19: Outline of the Approach
services can communicate and potentially negotiate the actions taken
INVITE + acceptable actions
  I’d like to invite you. If you cannot accept it, choose one of the actions.
  Callee may
    accept the call
    select one of the offered actions
    refine some of the actions and suggest them to the callee
    decline the call because of privacy issues

## Slide 20: The Approach in Action
caller
callee
INVITE (forward,recall)
SUGGEST(forward – mobile,
forward – voicemail)
INVITE(forward – voicemail)
SUGGEST(forward – voicemail – home
forward – voicemail - office
INVITE(forward – voicemail – home)
200 OK
ACK

## Slide 21: Results
Approach resolves effectively clashes between services belonging to different users
interaction avoidance rather than detection & resolution
extendable technique
‘classical interactions’ between services, such as Call Forwarding, Call Screening, Call Waiting, etc are avoided
new capabilities such as Call Clamping, or Forking can be expressed and hence be considered

## Slide 22: Conclusions
Feature Interactions are an issue in SIP
SIP allows for services to communicate
new approaches possible  negotiation
caller offers a certain set of acceptable actions
callee selects some of them and possibly offers some more detailed options
issues of privacy and trust
both parties need to understand the used vocabulary
Further work: How to create and store the necessary data for runtime use.
Can we include some ‘looking ahead’?